## Slide 1: Past and new technological developments at LOV for core and new BGC applications
E. Leymarie, A. Poteau, C. Penkerc’h, N. Alem, A. Pierret, V. Taillandier, F. D’Ortenzio, H. Claustre
Laboratoire d’Océanographie de Villefranche

## Slide 2
Acknowledgements
LOV : Antoine Poteau, Christophe Penkerc’h, A. Pierret, V. Taillandier, N. Alem, F. D’Ortenzio, H. Claustre
Strong and good collaboration with Ifremer and NKE
Technological developments are always a team work !

## Slide 3
Presentation Outline
Provor CTS4 : A float developed for the BGC core Argo mission
Provor CTS5 : A float developed for R&D and demanding application
  R&D facilities at LOV
  Past developments
  On going developments
Conclusion and perspectives.

## Slide 4
Nice results:
More than 200 floats
First float “Full BGC” deployed
Highly flexible BGC Argo float
 But not easy to explore new applications
              Development of the CTS4 profiler
Collaboration LOV – IFREMER - NKE

## Slide 5
              Development of the CTS5 profiler
How to integrate safely, at LOV, new applications ?
   dual board strategy. The CTS5 support a protocol to communicate with a user electronic board.
Modifiable at LOV = Flexibility
Stable = Security
Sensors
Float
Collaboration LOV - NKE

## Slide 6
Global checking
Failure mode
Data acquisition bias
              Development of the CTS5 profiler
How to test our development ?
1- Hardware Bench Simulator

## Slide 7
              Development of the CTS5 profiler
How to test our development ?
2- In-situ testing at LOV
1 000 m depth at 4 nm
2000 m depth at 10 nm
Good weather and predictable current for recovery

## Slide 8
              CTS5 profiler
              Past and on-going developments
ProVal float
ProIce float
UVP6 sensor
Passive acoustic

## Slide 9
              ProVal: A new float for radiometric measurements
Ed-Lu (7λ)
GPS & Iridium antenna
temperature & salinity
pressure
OCR507-IR
syntactic foam
ECO
external bladder (buoyancy)
tilt & compass (Internal)
surface
21 cm
24 cm
height : 213 cm
width : 138 cm
weight : 65 kg
65 cm
  Irradiance (Ed) and radiance (Lu) at 7 wavelength [380 - 665 nm]
Tilt and compass sensors
Chla, backscattering, CDOM, CTD
Already 3 floats and more than 600 profiles. Frontiers in mar. Sc.
https://www.frontiersin.org/articles/10.3389/fmars.2018.00437/full
 Next : integration of Hyperspectral radiometer (EA-RISE)
3 weeks deployment with HCMR

## Slide 10
Crédit P. Bourguain
              ProIce: A BGC float for arctic condition
Joint work with C. Marec, J. Lagunas, E. Rehm and M. Babin from Takuvik
Ice avoidance : ISA adapted to Baffin Bay, Altimeter and date criteria programmed on the LOV acquisition board
Change of configuration under-ice (date criteria)

## Slide 11
Crédit P. Bourguain
              ProIce: A BGC float for arctic condition
Joint work with C. Marec, J. Lagunas, E. Rehm and M. Babin from Takuvik
Ice avoidance : ISA adapted to Baffin Bay, Altimeter and date criteria programmed on the LOV acquisition board
Change of configuration under-ice (script based - date criteria)
 Next : Move to a more industrialized version.

## Slide 12
UVP6-LP : Miniaturized Under Vision Profiler
 Article soumis à Frontiers
Projet GOPPI
Low power, image based, particle size counter (18 size class, 64 to 4100 µm)
Sensor developed at LOV M. Picheral et al.
 Next : Finalize industrialized version.

## Slide 13
Passive Acoustic Monitoring
acoustic monitoring
cetacean
Wind
Rain
Ice
BGC - Argo
anthropic
Estimate wind speed and rainfall from parking depth
Passive acoustic recorder (RTSys) and transmission of 30 FFT bands (1/3 octave) per acquisition
Several short deployments (1 week)
Joint work with J. Bonnel (Whoi) and D. Cazau (ENSTA)
Color = time scale
 Next : achieve longer deployments (ERC – REFINE)

## Slide 14
Overview and future developments.
Conclusion on the acquisition board managed by LOV
  Created a lot of opportunities for testing new applications
  But difficulties when you want to industrialize these applications
 New Development with NKE : CTS5 - USEA
  Increased capabilities for BGC-Core Argo
    Mission and sampling flexibilities
    Increased Rudics speed
    GUI configuration tools
  Room for new applications developed by LOV but with easier industrialization
    New sensor
    Advanced On-Board Processing

## Slide 15
CTS5 – USEA : First Results
Integration of the UVP6 sensor as commercial product
Thanks to C. Schmechtig, JP Rannou and T. Carval for data handling

## Slide 16
Perspectives
A lot of new applications are waiting to be implemented on floats
Very significant progress is being made to reduce sensor power consumption (ex. UVP  20 times less in 10 years) opening new applications for Argo floats
The bottleneck for the next decade is the telemetry !
Chart: Years
| 1990 | 1993 | 1994 | 1995 | 1997 | 2001 | 2002 | 2004 | 2020
Home Internet | 4.8 | 14.4 | 28.8 | 56 | 512 | 1024 | 2048 | 6144 | 512000
Iridium Rudics | 2.4 | 2.4 | 28.8 | 28.8
Rudics
Iridium Certus 20
Iridium Certus 100
 Need to work on “On-board processing” for images, sound identifications, data reduction, …

## Slide 17: Merci